## Slide 1
MuJoCo Numerical Simulation Framework for SDAS Hands
Yushuo Wang | Synergy Hand Simulation | Physical Simulation Final Poster
Problem Statement
Literature Review
Methodology
Experimental Results
Conclusion
Goal: replace geometry playback with MuJoCo numerical integration.
Inputs: .ohd simulation definition, hand model path, time step, duration, driver time series, and distribution type.
Outputs: joint trajectories, target-vs-state error, contact count log, generated MJCF audit file, and rendered MuJoCo screenshots.
Constraint: the upgraded physics path must not include damper elements, viscous joint terms, tendon velocity friction, or hand-written -D qdot forces.
Why geometry was insufficient
The previous viewer directly assigned qpos from the synergy solver. It showed the intended pose, but skipped inertia, joint limits, MuJoCo constraints, and time evolution.
The new path treats the geometry solution as q_ref and lets MuJoCo integrate the actual q(t).
Success criteria implemented
1. .ohd file drives MuJoCo with time-varying driver inputs.
2. SDAS maps low-dimensional drivers into joint-space references.
3. No damping/damper/velocity actuator terms appear in generated MJCF.
4. At least two rendered postures and a geometry-vs-numerical comparison are generated automatically.
SoftHand 2 provides the numerical-model motivation, while SDAS provides this project's no-damper transmission abstraction.
Key equations retained
Postural synergy: q = S sigma
Adaptive transmission: R q = x, tau = R^T tau_M
Free-motion mapping: S_R = E^-1 R^T (R E^-1 R^T)^-1
MuJoCo target: q_ref(t) = B_sigma sigma(t)
Terms intentionally excluded
No joint viscous friction F qdot.
No tendon viscous friction or sliding-speed friction state.
No damper transmissions or dynamic-synergy damper model.
No PD/PI velocity feedback; position tracking uses only Kp(q_ref - q).
SDAS interpretation
Dual-ended tendon routing gives two path-dependent transmission vectors R_A and R_B. Their Schur-complement solution yields common-mode closure and differential reconfiguration without adding damper hardware.
Three-layer interface: distribution -> driver command -> MuJoCo execution.
SoftHand 2 Eq. 43
Dynamics structure
SDAS Schur map
B_sigma
.ohd time series
sigma(t)
MuJoCo mj_step
q(t), logs
Numerical control law
1. Interpolate each driver sample at time t.
2. Position inputs set sigma; velocity inputs integrate into sigma; force inputs map directly to joint generalized forces.
3. Compute q_ref = B_sigma sigma.
4. Apply tau = Kp(q_ref - q) + force_scale B_sigma f_sigma.
5. Advance only with MuJoCo mj_step; save q, q_ref, qdot, tau, and ncon.
Implemented user entry point
python scripts/run_mujoco_sdas.py "models/ohd test/mujoco_sdas_step.ohd"
Demo: three-finger gripper B, SDAS distribution, two time-varying drivers.
t = 0.35 s: common-mode closure
t = 1.05 s: differential SDAS posture
Geometry target q_ref (dashed) versus MuJoCo state q(t), plus RMS difference.
Quantitative check
600 MuJoCo steps at dt = 0.002 s; 9 hinge joints; 2 SDAS drivers.
RMS target-state difference = 0.1848 rad; max absolute difference = 0.5661 rad.
Generated MJCF audit: no damping, damper, or velocity actuator terms.
Outcome
The project now supports an .ohd-driven MuJoCo numerical simulation path that preserves SDAS synergy mapping while removing damper-related computations.
The interface separates model, driver sequence, distribution type, numerical settings, and output assets, making repeated experiments reproducible.
Next engineering step: extend endpoint distributions to task-space objectives and add optional contact-force postprocessing when grasp objects are introduced.
Sources: Della Santina et al., IEEE TRO 2018; project SDAS derivation; synergy_hand_sim MuJoCo SDAS demo run on 2026-06-03.